## Slide 1: Healthy Brain Study wearable data requests, integration, synchronization and access
Frederik D. Weber
Rayyan Tutunji

## Slide 2: Goals
preprocess raw data from wearable/mobile devices
synchronize data
In a software for data access requests
python

## Slide 3: Codename
wearanize "wearable data -> synchronize"

## Slide 4: Codename
wearanize "wearable data -> synchronize"
Its weara nize!

## Slide 5: Wearable devices and data
Hypnodyne zmax
  Accelerometer (3-Dimensional, -2 to 2 g, 256 Hz)
  Heart (Photoplethysmography or blood volume pulse BVP, 256 Hz)
  EEG/EOG (2 channels, forehead)
  battery
Empatica E4
  Accelerometer (3-Dimensional, -2 to 2 g, 32 Hz)
  Heart (Photoplethysmography or blood volume pulse BVP, 64 Hz)
  Electordermal activity (EDA, 4 Hz)
  Temperature skin (4 Hz)
activPAL
  Accelerometer (3-Dimensional, -2 to 2 g, 20 Hz)
EMA mobile survey app
  Timestamps (start_beep, end_beep) with questionnaire answers

## Slide 6: Steps (a wearanize plan)
0: parsing the file structure and finding the relevant wearable files
1.1: reading, preprocessing, concatenation and data export
1.2: checking data and file structure integrity
2.1: recording date and time extraction
2.2: data quality extraction
3: internal representation for computation and feature generation
4: common feature/modalities generation (for synchronization)
5.1: aligning and synchronization
5.2: align and synch info generation
6.1: find all relevant data given a request command line software
6.2: get the relevant files and snippets
6.3: visualize alignment and data availability
6.4: (optional) merge all the data in a common data format

## Slide 7: step 0: parsing the file structure and finding the relevant wearable files
storing in an wearabout.csv: ['subject_id', 'filepath', 'period', 'datatype', 'device_wearable', 'session']
status: done, needs testing on all data
QUESTION: read-only access to full data?

## Slide 8: HB root folder structure for wearables
sub-HB0136338856769 --|date_visit1.txt --|date_visit2.txt --|date_visit3.txt --|crf --|lab-1 --|lab-2 --|lab-3 --|pre-1 --|--|app --|--|--|sub-HBEMA5183016_pre-1_app-ema.csv --|--|wrb --|--|--|sub-HB1AP1618436_pre-1_wrb_apl.datx --|--|--|sub-HB1AP1618436_pre-1_wrb_apl.pml --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_combined_pd_data.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_combined_wk_data.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_logdata.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_slnwlist.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_sumdata.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_tagged_events.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_valid_periods.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl-evs.csv --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_01.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_02.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_03.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_04.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_05.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_06.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_full.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_01.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_02.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_03.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_04.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_05.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_06.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_1.zip
--|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_1_merged.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_2.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_3 - empty.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_4.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_5.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_6.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_7.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_raw.zip --|pre-2 --|pre-3 --|pst-1 --|pst-2 --|pst-3 --|qst sub-HB0139930729424 sub-HB0037923118974 sub-HB0063396839740 sub-HB0070445226012 sub-HB0087095682539 sub-HB0096744832326 sub-HB0108728545230 sub-HB0109563627639 sub-HB0116859417067

## Slide 9: step 1.1: reading, preprocessing, concatenation and data export
Hypnodyne zmax -> merging of channels in one file per session, saving as a zipped and compressed EDF
Empatica E4 -> merging all in one file per session to have data of multiple files in a timestamped csv
recreating wearabout.csv (with reprocessing the new exported files)
status: zmax & E4 and writing to zipped files done, activPAL & EMA in progress

## Slide 10: step 1.2: checking data and file structure integrity
e.g. if all the zmax file dates and data length make sense or need to be adjusted what files are present and which not but are expected
status: in testing for zmax and E4 data, missing activPAL and EMA
QUESTION: is there enough space to store the wearable data a second time? What about writing access? Separate file structure for writing?

## Slide 11: step 2.1: recording date & time extraction
extending wearabout.csv by info all devices: [... 'rec_start_datetime', 'rec_stop_datetime', 'rec_duration_datetime', 'sampling_rate_max_Hz']
status: done for zmax and E4, missing for activPAL and EMA
step 2.2: data quality extraction
[... 'data_quality_indicator' ] e.g.:
  Battery status at end of zmax
  SD of signals
  Proportion of flat lines
  or number of heart beats per recording duration
  ???
status: in progress for zmax and E4, missing for activPAL and EMA

## Slide 12: step 3: internal representation for computation and feature generation
Time series data (zmax, E4, activPAL) is put into similar data format (python mne.io.Raw format)
EMA data is retained as original format
status: zmax & E4 done, missing activePAL & EMA data (i.e. "filtering" of spreadsheets)
SUGGESTION: restructure EMA spreadsheet data into "long" format.

## Slide 13: step 4: common feature/modalities generation (for synchronization)
signals for alignment:
  continuous accelerometer signal (at 1 Hz)
  continuous heart rate signal (at 1 Hz)
zmax & E4 share PPG
  -> heart rate estimation
zmax & E4 & activPAL accelerometer
  -> integrated activity of 3-axis (at 1 Hz)
status: in progress for zmax and E4, needs testing, missing activPAL

## Slide 14: step 5.1: aligning and synchronization
Empatica is reference time for alignment (both PPG and accel.)
  activPAL alternative reference if only accelerometer is available
Algorithm: Cross-correlation in short segments to align data with common modalities
handles missing boundaries/data or gaps in synch data
indicates if the data is synchable
EMA data is not synchable (?)
status: general algorithm implemented for pairwise arbitrary signal alignment, missing alignment in a set of recordings
QUESTION: Are there some external cues, markers as reference for start of recordings?

## Slide 15: Aligning and synching
E4
zmax
activPAL
E4
zmax
activPAL
Best case
Often case
corrupted parts?
warping?
non-overlap/missing?
synch-reach?
non-linear warping?

## Slide 16: Simplified SYNCH algorithm
reference signal
reference signal
align signal
1
2
3
4
5
6
7
8
9
reference signal
2
3
5
6
8
9
offset
lag
lag
lag
Linear/non-linear prediction of lags = stretch/warp of the align signal
1
4
7
Unaligned due to inconsistent lags above tolerance
stretched align signal
reference signal
(In reality generated chunks overlap)

## Slide 17: step 5.2: align and synch info generation
extending wearabout.csv by info of all four devices: [... 'rec_start_datetime_reference', 'rec_stop_datetime_reference', 'rec_duration_datetime_reference', 'sampling_rate_max_Hz_reference_adaption']
status: not done
QUESTION: how to handle and representing non-linear warping? Will that matter?

## Slide 18: step 6.1: find all relevant data given a request command line software
Request via a software interface
  datetime start
  datetime stop
  subject ids
  visits(1|2|3|all)
  periods(pre-1|pre-2|pre-3|all)
  session(), datatype(wrb|app|all)
  wearables(zmx|emp|apl|ema|all)
  dateref(aligned|original)
  age(range)
  gender(m|f)
  …?
done by filtering wearabout.csv and create subset of wearaboutnow.csv
adding info to wearaboutnow.csv time offsets in seconds for each file
compiled python code via pyInstaller package
optional if data should be aligned or if the original times are requested
status: not done
admin@hbs-cluster: wearanize request -date-start='2018-09-12' …

## Slide 19: step 6.1: find all relevant data given a request (continued)
QUESTION: is age, gender, date of visit available in a spreadsheet?
  (date visit is available in files in the subfolder) sub-HB0136338856769 --|date_visit1.txt --|date_visit2.txt --|date_visit3.txt
  Where to get reliable annotation?
QUESTION: what are the selectable features to implement?

## Slide 20: step 6.2: get the relevant files and snippets
copy and load the relevant files for alignment into a temporary location together with the wearaboutnow.csv with paths relative to the temporary folder
status: not done
QUESTION: what other folders and info should be found for later copying? Should they also be parsed and preprocessed? How will the researchers access this data? QUESTION: is this enough support for researchers to work out the rest regarding the wearable and mobile app data?

## Slide 21: 6.3: visualize alignment and data availability
Quick overview of available data
…in a text: wearaboutnow.csv
…and visualized:
1
2
1
2
1
2
3
1
2
3
1
E4
zmax
activPAL
EMA
3
3
QUESTION: data quality also visible? What other features

## Slide 22: step 6.4: (optional) merge all the data in a common data format
resample of the data to align with the reference time line?
Costs a lot of computation and/or extra space needed by researchers to have a common format beyond the preprocessed?
empty periods are constant 0
zipped EDF (saves space)
EDF Annotations like EMA timestamps/ids
status: not done
QUESTION: shall this be attempted? Will people use the common data format?

## Slide 23: wearanize two step commands
wearanize init …  the preprocessing, done once in a while)
  Merge data and create wearabout.csv
  Recreate wearabout.csv
  Extend wearabout.csv with timestamp and quality data
  Extend wearabout.csv with subject-wise synch infos
wearanize request …  after init is done
  Parse wearabout.csv to fulfil request
  Create wearaboutnow.csv
  Copy requested files and wearaboutnow.csv to a final destination keeping folder structure (subject wise)
  Create a merged visualization
  (optional: merging and syncing of data in one format)
QUESTION: is it sufficient to process all only once, or needs to be processed "amended as data arrives"? Other functionalities?

## Slide 24: Remaining issues
Zmax original file attributes not available that stores original recording time?
  Information lost? Storing of all file attributes of the micro SD card files?
EDF reader (python MNE) fixes for zmax data to merge with main branch
Feature extraction and what to select from the activPAL data to export
Documentation of wearanize commands and code
Maintainability
Extendibility (more devices or data later?)