## Slide 1: Healthy Brain Study wearable data requests, integration, synchronization and access
Frederik D. Weber
Rayyan Tutunji

## Slide 2: Original Goals
preprocess raw data from wearable/mobile devices
synchronize data
In a software for data access requests
python

## Slide 3: Codename software:
wearanize "wearable data -> synchronize"

## Slide 4: Codename software:
wearanize "wearable data -> synchronize"
Its weara nize!

## Slide 5: Wearable devices and data:
Hypnodyne zmax
  Accelerometer (3-Dimensional, -2 to 2 g, 256 Hz)
  Heart (Photoplethysmography or blood volume pulse BVP, 256 Hz)
  EEG/EOG (2 channels, forehead)
  battery
Empathica E4
  Accelerometer (3-Dimensional, -2 to 2 g, 32 Hz)
  Heart (Photoplethysmography or blood volume pulse BVP, 64 Hz)
  Electordermal activity (EDA, 4 Hz)
  Temperature skin (4 Hz)
activPAL
  Accelerometer (3-Dimensional, -2 to 2 g, 20 Hz)
mobile survey app

## Slide 6: Steps (a wearanize plan)
0: parsing the file structure and finding the relevant wearable files
1.1: reading, preprocessing, concatenation and data export
1.2: checking data and file structure integrity
2.1: recording date and time extraction
2.2: data quality extraction
3: internal representation for computation and feature generation
4: common feature/modalities generation (for synch by overlap)
5.1: aligning and synchronization
5.2: align and synch info generation
6.1: find all relevant data given a request command line software
6.2: get the relevant files and snippets
6.3: optional, merge in a common data format all the data

## Slide 7: step 0: parsing the file stucture and finding the relevant wearable files
storing in an wearabout.csv: ['subject_id', 'filepath', 'period', 'datatype', 'device_wearable', 'session']
status: done

## Slide 8: step 1.1: reading, preprocessing, concatenation and data export
Hypnodyne zmax -> merging of channels in one file per session, saving as a zipped and compressed EDF
Empathica E4 -> merging all in one file per session to have data of multiple files in a timestamped csv
recreating wearabout.csv without reprocessing the new files
status: zmax & E4 done, activPAL & app in progress

## Slide 9: step 1.2: checking data and file structure integrity
e.g. if all the zmax file dates and data length make sense or need to be adjusted what files are present and which not but are expected
status: in testing
QUESTION is there enough space to store the wearable data a second time?

## Slide 10: step 2.1: recording date & time extraction
extending wearabout.csv by info all devices: [... 'rec_start_datetime', 'rec_stop_datetime', 'rec_duration_datetime', 'sampling_rate_max_Hz']
status: done for zmax and E4, activPAL missing
step 2.2: data quality extraction
[... 'data_quality_indicator' ] (e.g. Battery status at end of zmax, SD of signals or flat lines, or beat signals present per recording length)
status: in progress for zmax and E4, activPAL missing

## Slide 11: step 3: internal representation for computation and feature generation
Time series data (zmax, E4, activPAL) is put into similar dataformat (python mne.io.Raw format)
App data is retained as original format

## Slide 12: step 4: common feature/modalities generation (for synch by overlap)
signals for alignment: continuous heart rate signal (at 1 Hz) continuous accelerometer signal (at 1 Hz)
zmax & E4 share PPG
  -> heart rate estimation
zmax & E4 & activPAL accelerometer
  -> integrated activity
status: in progress for zmax and E4, needs testing, activPAL missing

## Slide 13: step 5.1: aligning and synchronization
Empathica is reference time for alignment
Cross-correlation in short segments to align data with common modalities
handles missing boundaries/data or gaps in synch data
indicates if the data is synchable
Status: general algorithm implemented for pairwise arbitrary signal alignment, missing alignment in a set of recordings

## Slide 14: Aligning and Synching
E4
zmax
activPAL
E4
zmax
activPAL
Best case
Often case
?

## Slide 15: Simplified SYNCH algorithm
reference signal
reference signal
align signal
1
2
3
4
5
6
7
8
9
reference signal
2
3
5
6
8
9
offset
lag
lag
lag
Linear prediction of lags = stretch of the align signal
1
4
7
Unaligned due to inconsistent lags above tolerance
stretched align signal
reference signal
(In reality generated chunks overlap)

## Slide 16: step 5.2: align and synch info generation
extending wearabout.csv by info of all four devices: [... 'rec_start_datetime_reference', 'rec_stop_datetime_reference', 'rec_duration_datetime_reference', 'sampling_rate_max_Hz_reference_adaption']
status: not done

## Slide 17: step 6.1: find all relevant data given a request command line software
Request via
  datetime start
  datetime stop
  subject ids
  visits(1|2|3|all)
  periods(pre-1|pre-2|pre-3|all)
  session(), datatype(wrb|app|all)
  wearables(zmx|emp|apl|app|all)
  dateref(aligned|original)
  age(range)
  gender(m|f)
  …?
done by filtering wearabout.csv and create subset of wearaboutnow.csv
adding info to wearaboutnow.csv time offsets in seconds for each file
compiled python code via pyInstaller package
optional if data should be aligned or if the original times are requested
status: not done
admin@hbs-cluster: wearanize -date-start='2018-09-12' …

## Slide 18: step 6.1: find all relevant data given a request (continued)
QUESTION: is age, gender, date of visit available in a spreadsheet?
  (date visit is available in files in the subfolder) sub-HB0136338856769 --|date_visit1.txt --|date_visit2.txt --|date_visit3.txt
  Where to get reliable annotation?
QUESTION: what are the selectable features to implement?

## Slide 19: step 6.2: get the relevant files and snippets
copy and load the relevant files for alignment into a temporary location with the wearaboutnow.csv with paths relative to the temporary folder
status: not done
QUESTION: what other folders and info should be found for later copying? Should they also be parsed and preprocessed? How will the researchers access this data? QUESTION: is this enough support for researchers to work out the rest regarding the wearable and mobile app data?

## Slide 20: step 6.3: optional, merge in a common data format all the data
resample of the data to align with the reference time line? costs a lot of computation and/or extra space needed by researchers to have a common format beyond the preprocessed?
status: not done

## Slide 21: Remaining issues
Zmax original file attributes not available
  Information lost? Storing of all file attributes of the micro SD card files?

## Slide 22: HB root folder structure for wearables
sub-HB0136338856769 --|date_visit1.txt --|date_visit2.txt --|date_visit3.txt --|crf --|lab-1 --|lab-2 --|lab-3 --|pre-1 --|--|app --|--|--|sub-HBEMA5183016_pre-1_app-ema.csv --|--|wrb --|--|--|sub-HB1AP1618436_pre-1_wrb_apl.datx --|--|--|sub-HB1AP1618436_pre-1_wrb_apl.pml --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_combined_pd_data.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_combined_wk_data.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_logdata.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_slnwlist.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_sumdata.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_tagged_events.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl_valid_periods.csv --|--|--|sub-HB1AP1618436_pre-1_wrb_apl-evs.csv --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_01.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_02.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_03.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_04.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_05.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_06.zip --|--|--|sub-HB1EM6570669_pre-1_wrb_emp_full.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_01.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_02.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_03.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_04.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_05.zip --|--|--|sub-HB1EM8057291_pre-1_wrb_emp_06.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_1.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_2.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_3.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_4.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_5.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_6.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_7.zip --|--|--|sub-HB1ZM3321037_pre-1_wrb_zmx_raw.zip --|pre-2 --|pre-3 --|pst-1 --|pst-2 --|pst-3 --|qst sub-HB0139930729424 sub-HB0037923118974 sub-HB0063396839740 sub-HB0070445226012 sub-HB0087095682539 sub-HB0096744832326 sub-HB0108728545230 sub-HB0109563627639 sub-HB0116859417067